## Slide 1: DWDM Network Planning Tool (Training-Level Feasibility Analyzer using FastAPI & React)
Presented by : Girish CK
Technology Stack : Python (FastAPI) React (Frontend UI)
Date : 23/02/2026

## Slide 2: Agenda
Introduction to DWDM
Planning Metrics
Power Budget & Rx Power
OSNR (Threshold & Margin)
System Design (FastAPI + React)
API Contract
UI Screens
Edge Cases
Lessons Learned & Future Work
Live Demo & Q&A
References

## Slide 3: Introduction to DWDM
These are the fundamental concepts required to understand DWDM network planning:
• Wavelengths ○ DWDM carries multiple optical channels over a single fiber ○ Each channel operates at a different wavelength (λ) ○ Enables high-capacity transmission
• Spans ○ A span is the fiber segment between two optical elements ○ Signal power reduces over distance due to attenuation ○ May include connectors, splices, and amplifiers
• ROADMs (Reconfigurable Optical Add-Drop Multiplexers) ○ Allow dynamic routing of wavelengths ○ Enable flexible optical network design

## Slide 4: Planning Metrics
Fiber Attenuation ○ Signal loss per kilometer (dB/km) ○ Increases with distance ○ Primary contributor to total link loss
• Connectors ○ Each connector introduces insertion loss ○ Accumulates across the link
• Splices ○ Fusion or mechanical joints in fiber ○ Add small but cumulative loss
• EDFA (Erbium-Doped Fiber Amplifier) ○ Compensates for fiber loss by amplifying signal power ○ Includes gain and practical penalties

## Slide 5: Power Budget & Rx Power
• Power Budget & Rx Power (Formula + Example)
• What is Power Budget? ○ Power Budget = Tx Power − Receiver Sensitivity ○ It represents the maximum allowable loss in the link.
• Total Link Loss ○ Total Loss = (Fiber Loss + Connector Loss + Splice Loss − Amplifier Gain) ○ Where: ▪ Fiber Loss = Length × Attenuation ▪ Connector Loss = Number of connectors × Loss per connector ▪ Splice Loss = Number of splices × Loss per splice
• Received Power ○ Rx Power = Tx Power − Total Loss ○ Power condition is satisfied if: ▪ Rx Power ≥ Receiver Sensitivity
• Example ○ Given: ▪ Tx Power = 2 dBm ▪ Receiver Sensitivity = −28 dBm ○ Power Budget = 2 − (−28) = 30 dB ○ Assume Total Loss = 22 dB ○ Rx Power = 2 − 22 = −20 dBm ○ Since −20 ≥ −28 → Power PASS

## Slide 6: OSNR (Threshold & Margin)
• What is OSNR? ○ OSNR (Optical Signal-to-Noise Ratio) measures the quality of the optical signal. ○ It represents the ratio of signal power to noise power. ○ Higher OSNR → Better signal quality.
• Simplified OSNR Estimation (Training Model) ○ Estimated OSNR = Tx Power − Total Loss + Total Amplifier Gain − Noise Penalty
• OSNR Margin ○ OSNR Margin = Estimated OSNR − OSNR Threshold
• Feasibility Condition ○ If OSNR Margin ≥ 0 → OSNR PASS ○ If OSNR Margin < 0 → OSNR FAIL ○ Both conditions must be satisfied: ▪ Rx Power ≥ Receiver Sensitivity ▪ OSNR Margin ≥ 0 ○ Only then → Link is Feasible
• Example ○ Assume: ▪ Estimated OSNR = 20 dB ▪ OSNR Threshold = 18 dB ○ OSNR Margin = 20 − 18 = 2 dB ○ Since margin ≥ 0 → OSNR PASS

## Slide 7: System Architecture

## Slide 8: Data Flow Diagram

## Slide 9: API Contract
Endpoint Information
HTTP Method: POST
URL : /api/plan/feasibility
Content-Type: application/json
Request Structure
{ "nodes": [ { "id": "A", "label": "Site A" }, { "id": "B", "label": "Site B" } ], "spans": [ { "from": "A", "to": "B", "length_km": 50, "connectors": 2, "splices": 6, "amplifier_gain_db": 10 } ], "service": { "tx_power_dbm": 0, "receiver_sensitivity_dbm": -26, "osnr_threshold_db": 18 }, "assumptions": { "fiber_atten_db_per_km": 0.22, "conn_loss_db": 0.5, "splice_loss_db": 0.1, "noise_penalty_db": 3.0, "amp_penalty_db": 1.0
}}
Response Structure
{ "total_loss_db": 3.6, "tx_power_dbm": -3.6, "osnr_margin_db": -15.6, "feasible": false, "per_span": [ { "span_index": 0, "from": "A", "to": "B", "length_km": 50, "loss_db": 3.6
} ],
"assumptions_used": { "fiber_atten_db_per_km": 0.22, "conn_loss_db": 0.5, "splice_loss_db": 0.1, "noise_penalty_db": 3.0, "amp_penalty_db": 1.0
}}

## Slide 10: UI Screens

## Slide 11: UI Screens

## Slide 12: Edge Cases
The planner was tested against critical boundary conditions to ensure robustness.
• Long Spans ○ Large fiber length increases attenuation ○ Total loss may exceed power budget ○ Rx power may fall below sensitivity
• No Amplifiers ○ No gain to compensate fiber loss ○ High probability of power failure ○ Critical over long distances
• Receiver Sensitivity Limits ○ Rx power must exceed sensitivity ○ Even if OSNR is acceptable ○ Otherwise results in failure
• High OSNR Threshold ○ Advanced modulation needs higher OSNR ○ Stricter quality requirements ○ May fail despite sufficient power

## Slide 13: Future Work
The current implementation is a simplified training model. Future enhancements can improve realism and scalability.
• Flex-Grid Support ○ Variable channel spacing ○ Flexible spectral allocation ○ Improved spectral efficiency
• Modulation-Aware Planning ○ Supports QPSK, 16QAM, etc. ○ Dynamic OSNR thresholds ○ Capacity-aware feasibility
• Regenerator (Regen) Planning ○ Identify regeneration locations ○ Support long-haul multi-span links ○ Improve signal quality
• Telemetry Integration ○ Use real-time performance data ○ Compare planned vs actual metrics ○ Enable adaptive optimization

## Slide 14: Demo

## Slide 15: References
Basic DWDM Concepts (Training Notes)
FastAPI Documentation
React Documentation
Axios Documentation
React Flow Documentation

## Slide 16: THANK YOU